PDC Tracking Abnormity

---
Experiment Layout
TOF Wall
2.24m
32D02
32Q01
PDCU0
PDCU1
PDCD0
PDCD1
MUSIC1
MUSIC0
x
z
TOF stop
target
8.45m
11.46m
DC0
DC1
DC2

---
BeamPos - PDCU0
B0

---
BeamPos - PDCU1
B0

---
BeamPos - Target

---
BeamPos - PDCD0

---
BeamPos - PDCD0

---
BeamPos - PDCD1

---
Rigid CUT
Commands that cut off the horizontal and verticla tails of beamPos at PDCU0:
treeTrack->Draw("PDCPos[2][1]:PDCPos[2][0]>>h(500, -100., 100., 500, -100., 100.)", "dsca11==0&&dsca[4]==1&&A0&&B0&&C0&&B2&&qdc[4]>30&&qdc[6]>30 &&nuTa[1][0][0]>=0&&nuTa[1][0][1]>=0&&nuTa[1][0][2]>=0&&nuTa[1][0][3]>=0&& chiTa[1][0][0]>-1.8&&chiTa[1][0][0]<0.1&&chiTa[1][0][1]>-1.8&&chiTa[1][0][1]<0.1&&chiTa[1][0][2]>-1.8&&chiTa[1][0][2]<0.1&&chiTa[1][0][3]>-1.8&&chiTa[1][0][3]<0.1 &&nuTa[1][1][0]>=0&&nuTa[1][1][1]>=0&&nuTa[1][1][2]>=0&&nuTa[1][1][3]>=0&& chiTa[1][1][0]>-1.8&&chiTa[1][1][0]<0.1&&chiTa[1][1][1]>-1.8&&chiTa[1][1][1]<0.1&&chiTa[1][1][2]>-1.8&&chiTa[1][1][2]<0.1&&chiTa[1][1][3]>-1.8&&chiTa[1][1][3]<0.1", "colbox")
Which translates into:
Each wire plane has a valid fired wire belonging to the track && the tracking residue is within 3sigma of the main peak of residue distribution.
Only 27% events survive the seemingly normal cut.

---
55312 v.s. 49668, out: 10.20%

---
13733 v.s. 13705, out: 0.20%

---
BeamPos – PDCD1

---
55312 v.s. 49555, out: 10.41%

---
BeamPos – PDCD1 – Rigid CUT

---
13733 v.s. 13674, out: 0.43%

---
Conclusion
For geometrical efficiency calculations of PDCs, we should resort to events with prime tracking qualities so as to be free from tracking errors.
Q.: Why is the mis-reconstructed positions distribute only horizontally and vertically?
A.: The track mis-reconstruction is a small probability event in X(Y) direction. So much more often than not it happens in X(Y) direction when tracking in Y(X) direction is normal. This is the reason why the tails in the beam position spectra don’t propagate in a slant way. The probability of tracking errors happening both in X and Y direction at the same time is much more lower than it is in either direction.